## Slide 1: Interlake Boat Measurement
A Step-by-Step Guide to Measuring Interlakes as of 2013

## Slide 2: General Rules
If a boat:
  does not appear on the database;
  has a new owner; or
  if the measurement value is “OK”,
it must be measured and the numerical values entered on the Measurement Form.
The measured value (in inches, not feet and inches) must be entered on the form.
Use the 2” mark on the tape measure rather than the absolute end, which could have wear or a right angle fitting.
Notes: If feet and inches are inadvertently entered, it’s not a disaster. The Chief Measurer is usually smart enough to figure out which is which.

## Slide 3: Measurement Form
Boat Mass
Spars
Hull
Safety
Measurement Committee Signoff
Competitor Signoff

## Slide 4: Hull
Rudder
  Type (Regular or Spade)
  Mass (excluding tiller)
    8.0 lbs minimum
Deck Type
  1,2,3,4,5, or 6 (Custom)
Deck Material
  Wood or Fiberglass
Floorboards
  Yes or No. “Yes” means permanent. Removable floorboards must be removed before the boat is weighed.

## Slide 5: Hull (cont)
Mast Step – Distance from Bow to forward face of mast
  76.0” minimum
Reduced CB Trunk Height
  14.5” minimum
Chainplate Position
  99 – 101” (Older boats at 99 – 106” are OK)
Spinnaker Pole Length
  84 – 97”
CB Pivot Bolt Position
  91.5 – 95.5” (213.5” minus the distance between the Bolt and the transom measured along the curvature of the hull)

## Slide 6: Rudder
The regular rudder must be laid on the template in such a way that the edge “breaks” all of the blue circles.
                There are very few of the rectangular “spade” rudders left in use.
Weigh the rudder on the scale used for weighing the boats or other suitable scale.
DO NOT include the tiller when weighing.
A rudder weighing less than 8.0 lbs. cannot be corrected by adding a corrector weight. Adding a weight does not add strength.
Rudder Type is: “Regular” or “Spade”
Rudder must also be weighed (8.0 lb minimum)

## Slide 7: Deck Types
Deck Type 1
Original fiberglass deck from Station 8 to Station 16. #160 - 460 No seats. May have floorboards over entire cockpit May have a wooden splash rail.

## Slide 8: Deck Types
Deck Type 2
Original seated fiberglass deck from Station 8 to Station 16.

## Slide 9: Deck Types
Deck Type 3
Extended seated deck. Cockpit extends from Station 7 to Station 18 #1040-? Seats extend to transom.

## Slide 10: Deck Types
Deck Type 4
Flush "Racing" deck. Hull #1300+ Cockpit extends from Station 7 to Station 16

## Slide 11: Deck Types
Deck Type 5
Newer seated deck #1300+. Similar to 4, but with seats.

## Slide 12: Deck Types
Deck Type 6
Custom or home built. (#1000 shown). Notice rolled side deck (not beveled) and forward edge of cockpit.

## Slide 13: Spinnaker Pole
Pole Length
Overall length, tip-to-tip
Not inside-to-inside
Not inside-to-outside

## Slide 14: Mast Position
Bow Point
The intersection of the hull and deck.
DOES NOT include the rub rail.
Front of Mast
The front of the mast itself
NOT the mast step.
76” minimum.
Most boats are 76-76.25”

## Slide 15: Chain Plate
Bow Point
The intersection of the hull and deck.
DOES NOT include the rub rail.
Front or Rear of Chain Plate
Place the measurement stick ahead or behind both chain plates (Ahead shown)
Measurement
Where stick crosses the tape, add or subtract ½” for half the width of the chain plate fitting (99.75 + 0.50 = 100.25” as shown at right.
0.50”

## Slide 16: Cockpit Dimension
Requirement
16.5” in from the edge of the deck (excluding rub rail) a vertical line downward must hit the hull, not anything permanently attached to the deck.
Visual Inspection
Keep an eye out for added jib fairlead tracks.
A moveable jib car that extends into this area IS NOT A VIOLATION
J OK
L Not OK

## Slide 17: Centerboard Trunk
Non-enclosed Trunks
Measure from the bilge to the top of the trunk
14.5” minimum
Enclosed Trunks
Enter “99” on the form.
Need Picture

## Slide 18: CB Pivot Bolt
Performed on hoist while weighing
2 person operation
The stick is inserted into the trunk and held alongside the board against the CB Pivot Bolt.
Stick is bent along the hull and the measurement made at the transom.
Subtract the number from 213.5” and enter the result on the form.
Need Pictures

## Slide 19: Spars
Lower Mast Band – Distance from Deck (inc. Mast Step Thickness)
  21.5 to 22.5”
Upper Mast Band – Distance From Lower Band
  21’ (252”) maximum
Boom Band – Distance from Mast
  12’ 3” (147”) maximum
Spinnaker Hoist – Distance from Deck to Upper side of sheeve.
  18’ 6” (222”) maximum

## Slide 20: Lower Mast Band
Usually, the 2” mark should be placed 3/8” below the butt of the mast to account for the 3/8” thickness of the mast step.
The measurement must be taken from the upper side of the band to the nearest 1/8” (Here, 24.5”, minus 2” for the tape measure equals 22.5” entered on the form.

## Slide 21: Upper Mast Band
The measurement is made to the lower edge of the upper band. Subtract 2” because the upper end of the lower band is at the 2” point and enter the resulting number (i.e. 252.0”)
Place the 2” mark on the upper edge of the lower mast band.

## Slide 22: Boom Band
The older, adjustable gooseneck should be measured from the track that runs up and down on the mast. No allowance for gooseneck.
The most common gooseneck is 1.5” from the back of the mast to the face of the boom
The measurement is taken from the face of the boom to the inside of the boom band. The minimum is 147”, including the 1.5” of the gooseneck at left. Enter the number in inches (i.e. “147.25”, not “12’ 3.25”)
1.5”
Add 1.5” for gooseneck

## Slide 23: Spinnaker Hoist
The measurement is made to the top of the sheeve when lying flat against the mast. The maximum is 18’ 6” or 222”. Remember to subtract the 2” for the bottom measurement.
Place the 2 3/8” mark on the upper edge of the lower mast band to account for the 3/8” mast step.